## Slide 1
ABSTRACT:
Concrete is the most widely used composite construction material. Fine aggregate plays a very important role for imparting better properties to concrete in its fresh and hardened state. Generally, river sand was used as fine aggregate for construction. Due to the continuous mining of sand from riverbed led to the depletion of river sand and it became a scarce material. Also, sand mining from river bed caused a lot of environmental issues. As a substitute to river sand, manufactured sand has been used.
In this present experimental study, a comparative study has been carried out to check the usability of manufactured sand in place of natural sand. This study involves determination of some major properties of concrete like compressive strength, split tensile strength, flexural tensile strength and durability in acidic medium made of both the sands.
Based on proposed studies, quality of manufactured sand is equivalent to natural sand in many respects, such as cleanliness, grading, strength, angularity, specific gravity. Conclusion have been arrived that manufactured sand produced from VSI (vertical shaft impactor) is a suitable and viable substitute to river sand and could be effectively used in making concrete which provides adequate strength and durability for the concrete.
In the design of concrete structures, concrete is taken into account by taking its compressive strength value. The compressive strength of the concrete made of manufactured sand is observed to be very nearer to the strength of the concrete made of natural sand in the present investigation, there by 100% replacement is reasonable.

## Slide 2
AIM
Fine aggregate is the essential material to prepare concrete, due to most number of constructions the percentage of fine aggregate is reduced. The world requires a solution for this problem. In this situation the robo silicon was the first company to brand its sand as “ROBOSAND TM.” This became the revolution in construction field as a replacement of fine aggregate. Robo sand is suitable upto a certain percentage.
INTRODUCTION
This chapter contains the general information about manufactured sand, its origin, need of manufactured in construction. It also includes the exact meaning of manufactured sand, crushed dust, process of manufacturing by various machinery.Natural sands are weathered and worn-out particles of rocks and are of various grades or size depending on the accounting of wearing. The main natural and cheapest resource of sand is river. Dams are constructed on every river hence these resources are erasing very fast. Now a day's good sand is not readily available, it should be transported from long distance. Those resources are also exhausting very rapidly.
Sand is the one of main constituents of concrete making which is about 35% of volume of concrete used in construction industry. Natural sand is mainly excavated from river beds
and always contain high percentage of in organic materials, chlorides, sulphates, silt and clay that adversely affect the strength, durability of concrete & reinforcing steel there by reducing the lifeof structure, when concrete is used for buildings in aggressive environments, marine structures, nuclear structures, tunnels, precast units, etc. Fine particles below 600 microns must be at least30% to 50% for making

## Slide 3
concrete will give good results. Normally these particles are not present in river sand up to required quantity. Digging sand, from river bed in excess quantity is hazardous to environment. The deep pits dug in the river bed, affects the ground water level. The sand in the mortar does not add any strength but it is used as an adulterant for economy and with the same it prevents the shrinkage and cracking of mortar in setting. The sand must be of proper gradation (it should have particles from 150u to 4.75 mm in proper proportion). When fine particles are in proper proportion, the sand will have lessvoids. The cement required will be less when there will be less void in sand. Such sand will be more economical. Only sand manufactured by V.S.I. Crusher is cubical and angular in shape. Sand made by other types of machines is flaky, which is troublesome in working. There is no plasticity in the mortar. Hence the mason are not ready to work with machine made crushed stone sand. For the same reason inferior river sand may be used. Manufacturing sand from jaw crusher, cone crusher, roll crusher often contains high percentage of dust and have flaky particle. Flaky and angular particles may produce harsh concrete, and may result in spongy concrete. There isstandard specification for Fine aggregates (Sand). It is divided in four gradations. Generally known as Zone I, Zone II, Zone III and Zone IV. There is sieve Designation for each grade. Gradation is made as per the use of the sand. V.S.I can produce any zone of sand. But in case of natural sand quality varies from location to location without any control.

## Slide 4
MATERIALS:
Fine Aggregate / Robo sand
Course aggregate
Cement
Water
TESTS CONDUCT:
Workability by slump cone test
Compressive strength test
Spliƫng tensile strength test
Flexural tensile strength test
Durability of concrete